## Slide 1: SIRV-Based High-Resolution PolSAR Image Speckle Suppression via Dual-Domain Filtering
IGARSS 2019
Yexian Ren, Lingli Zhao , Jie Yang, Pingxiang Li, Lei Shi
E-mail：renyexian@foxmail.com
work done at
Wuhan University

## Slide 2: Significance of PolSAR Speckle Filtering
An important topic in SAR image processing
estimating physical/polarization parameters; image segmentation; target detection; classification and terrain interpretation
Original 4-look PolSAR image
After 7*7 Refined Lee filter
Random fluctuation of speckle leads to centroid aliasing of different scattering mechanisms
AIRSAR L-band
San Francisco
Speckle Suppression

## Slide 3: Related work
PolSAR speckle filter (TGRS 2010~2017)
SDAN (IDAN+SIRV), [Vasile et al. 2010]
Nonlocal pretest (Wishart-based) , [Chen et al. 2011]
Nonlocal pretest + Lee, [Zhong et al. 2014]
Generalized meanshift (meanshift+sigma+LMMSE), [Lang et al. 2014]
Adaptive size window + Lee (homogenous index), [Lang et al. 2015]
NL-SAR (Nonlocal + Wishart Kernel + LMMSE), [Deledalle et al. 2015]
Extended Sigma (Rayleigh-based), [Lee et al. 2015]
ACM (boxcar+SIRV+local heterogeneity coefficients), [Yang et al. 2016]
POSSC (patch ordering+simultaneous sparse coding), [Xu et al. 2016]
GMM + Nonlocal, [Wang et al. 2017]
5/10 specifically discussed the heterogeneity and high-resolution PolSAR images.

## Slide 4: Resolution: Medium/low VS High
Heterogeneous regions in high resolution images
High resolution inevitably leads to heterogeneous clutter
Larger resolution unit
(sufficient elementary scatterers)
central limit theorem，CLT;
Gauss model is used to model the echo complex vector.
The amplitude obeys Rayleigh distribution and the multilook coherency matrix obeys Wishart distribution.
Smaller resolution units
(elementary scatterers is not sufficient)
Low grazing angle + narrow-beam
(non-stationary reflectivity)
Heterogeneous clutter

## Slide 5: An interesting viewpoint about heterogeneous sea clutter
viewpoint：Sea surface waves can be decomposed into surface tension waves with micro scale and gravity waves with macro scale.
Tension wave results in fast-changing characteristics of clutter (millisecond order), i.e. speckle component.
Gravity wave results in slow-changing characteristics of clutter (second order), i. e. texture component (modulation component).
Heterogeneous sea clutter can be regarded as the result of amplitude modulation of tension wave by gravity wave.
: texture (RCS)
s: speckle
Notes: The explanation of the sea clutter decomposition inspired me to do this work.

## Slide 6: Understanding of high-resolution PolSAR image
PauliRGB
texture (RCS)
speckle (include polarimetric)
The high-resolution PolSAR image can be regarded as the result of amplitude modulation of the fast-changing Gaussian random speckle (contains polarization information) by the slow-changing texture (RCS).
Texture (One dimensional nonnegative scalar)
RCS change in macro scale
Gaussian random speckle (Three dimensional normalized complex coherency matrix)
Coherent superposition of many random scatterers in micro scale.
Clutter decomposition diagram

## Slide 7: Clutter decomposition/SIRV based PolSAR dual-domain filter
Based on the viewpoint of the SIRV model, a dual-domain filter is designed, which takes full advantage of the clutter decomposition to decompose the task of PolSAR speckle suppression into polarimetric domain filtering and texture domain filtering.
After filtering in polarimetric domain and texture domain, the normalized coherency matrix is re-modulated by reconstructed texture.

## Slide 8: Details of dual-domain filter
Polarimetric Domain Filtering
Pre-estimation
polarimetric and texture prior
Patch match
location of selected samples
fixed-point iteration
T is often single-look coherency matrix format.

## Slide 9: Details of dual-domain filter
Texture domain filtering
PWF
Refine the texture by
SAR-POTDF
Sparse reconstruction
SAR-POTDF: B. Xu et al. "Patch Ordering based SAR Image Despeckling via Transform-Domain Filtering" IEEE J. Sel. Topics Appl. Earth Observ. Remote Sens., vol. 8, no. 4, pp. 1682–1695, Apr. 2015.

## Slide 10: Details of dual-domain filter
High-resolution PolSAR image reconstruction
M
Three-dimensional complex Gauss random speckle is suppressed sufficiently;
The stable state of polarization information is obtained.
The polarimetric coherency matrix is amplitude modulated by texture information.

## Slide 11: CETC-38 X band 0.1×0.4m data in Hainan

## Slide 13: Normalized coherency matrix in Pauli-RGB
SIRV estimator result
Dual-domain filter result

## Slide 14: CETC-38 X band 0.1×0.4m data in Hainan

## Slide 15: CETC-38 X band 0.1×0.4m in Hainan
The effect of processing single-look high-resolution PolSAR image is excellent.
Even when dealing with complex scenarios, it is still robust.

## Slide 16: DLR FSAR S band 0.5×0.6m data in Kaufbeuren

## Slide 18: IECAS C band 0.13×0.19m data in Zunhua

## Slide 19: DLR ESAR L band 3×3m Oberpfaffenhofen

## Slide 20: Gaofen-3 C-band Xi’An City

## Slide 21: Gaofen-3 C-band Xi’An City (after dual-domain filtering)

## Slide 22: GF3 Sea scene reconstruction: ships and waves (using dual-domain filter)

## Slide 23: Comparisons
Improved Sigma
Nonlocal pretest
Mean shift
Dual-domain

## Slide 24
Improved Sigma
Nonlocal pretest
Mean shift
Dual-domain

## Slide 25: Mean and standard deviation of separated multiplicative noise (Ratio)
Theoretical value: 。
If deviates too much from 1, it shows radiation distortion.
If far less than 1，the speckle suppression is not complete.
If is greater than the theoretical value, the results deviate from the true RCS.
Calculate on 1000800 single-look PolSAR image

## Slide 26: ENL in homogenous region: From 1 to 100
ENL of the original single-look PolSAR image
ENL of the filtered PolSAR image

## Slide 27: Novak’s polarimetric whitening filter results
Structural information extracted from the original image
(including a lot of natural clutter in homogenous region)
… the dual-domain filtered image
(almost no natural clutter in homogenous region)

## Slide 28: Polarimetric entropy
81-look
dual-domain filter

## Slide 29: Effect on the H/alpha/A

## Slide 30: Effect on the PolSAR data classification
AIRSAR L flevoland PolSAR data
PolSAR dual-domain filter result

## Slide 31: Effect on the PolSAR data classification
Groundtruth;
150 pixels in each class are randomly selected as training samples.

## Slide 32: Dual-domain filter + Random Forest Classifier
The nine channels of the dual-domain filtered coherency matrix are directly input into the random forest without any feature extraction.
If some feature extraction methods are applied, the classification result will be further improved.
Correct Rate: 0.9822
Kappa index: 0.9795

## Slide 33: Boxcar 5*5 + Random Forest Classifier
Correct Rate: 0.9225
Kappa index: 0.9112
The nine channels of the dual-domain filtered coherency matrix are directly input into the random forest without any feature extraction.
If some feature extraction methods are applied, the classification result will be further improved.

## Slide 34: Comparison of Classification Details
Dual-domain Filter+classifer
Boxcar 5*5+classifer
Pauli-RGB block of original PolSAR data
Clear
Blur

## Slide 35
AIRSAR L flevoland PolSAR data
dual-domain filter result

## Slide 36
dual-domain filter + RF classifer
Correct Rate:0.9696; Kappa Index: 0.9640
Boxcar5*5 + RF classifer
Correct Rate:0.9485; Kappa Index: 0.9392

## Slide 37
EMISAR L foulum PolSAR data
PolSAR dual-domain filter result

## Slide 38
dual-domain filter + RF classifer
Correct Rate:0.9157; Kappa Index: 0.8901
boxcar filter 5*5 + RF classifer
Correct Rate:0.8701; Kappa Index: 0.8329

## Slide 39: GF3-Xi’An
The scene is divided into five classes.
150 pixels in each class are randomly selected as training samples.
The nine channels of the dual-domain filtered coherency matrix are directly input into the random forest without any feature extraction.

## Slide 40
GF3-Xi’An classification

## Slide 41: Limitations
The computational load of the dual domain filter is very large.
Basic assumptions of SIRV: All polarization channels share the same texture.
P-band high-resolution PolSAR radar has strong penetration. When H-polarized and V-polarized electromagnetic waves penetrate some objects, their attenuation rates are different. The different textures may be observed in different polarization modes .

## Slide 42: IECAS P band PolSAR data experimental result
The dual-domain filter may fail when SIRV model and PWF are physically invalid.
The experimental result shows that the dual-domain filter is still effective for speckle suppression, but it may lead to blur when dealing with some distributed targets.

## Slide 43: When there is ambiguity on the PolSAR image
Dual-domain filter is difficult to deal with the ambiguity of the image itself.
FSAR X band
Original data
dual-domain filter result

## Slide 44: Changjiang Bridge in Wuhan (GaoFen-3)
Origin
After filtering

## Slide 45: Conclusion
One of the challenges in processing high-resolution PolSAR images is the entanglement of texture and speckle. The dual-domain filter based on clutter decomposition can achieve a good balance between the detail preservation of texture and suppression of speckle.
After the dual-domain filtering, a high signal-to-clutter ratio filtering result can be obtained. This will contribute to the further processing and application of PolSAR data, such as classification and segmentation.
One of the obvious limitations of the dual-domain filter is that the computational load is very large.
If you are interested in this work, you can refer to the following paper for more details:
Y. Ren, J. Yang, L. Zhao, P. Li and L. Shi, "SIRV-Based High-Resolution PolSAR Image Speckle Suppression via Dual-Domain Filtering," IEEE Trans. Geosci. Remote Sens., vol. 57, no. 8, pp. 5923-5938, Aug. 2019.

## Slide 46
Thank you!
renyexian@foxmail.com